c GEOS/DR100 Header descriptions                       February 27, 1987

cccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccc
c
c  Integer*2 header offset:
c
c    1  ! Number of extra integer blocks (blocksize=512 bytes)
c    2  ! Number of ASCII blocks
c    3  ! "Undefined" integer value (INULL)
c?   4  ! Data type: positive=real, negative=integer, abs. val.=#bytes/sample
c       !    except 1=R*4, INULL=I*2
c    5  ! If 1 then (*) parameters are defined
c
c   10  ! Year of event
c   11  ! Day of event (Julian)
c   12  ! Hour of event
c   13  ! Minute of event
c   14  ! Second of event
c   15  ! Milliseconds of event
c   16  ! Microseconds of event
c   17  ! Sample number of first tickmark
c   18  ! Detection amplitude of tickmark
c   19  ! Number of tickmarks detected
c   20  ! Serial number of recording unit
c   21  ! Event sequence number
c
c!  27  ! First active channel number recorded on unit
c!  28  ! Actual channel number as recorded on unit
c!  29  ! Total number of channels recorded on unit
c!  30  ! Total number of components recorded for station I.D.
c   31  ! Number of data records that follow
c   32  ! Index of last sample in last record
c?  33  ! Record size (bytes)
c?  34  ! Playback program (1=RDGeos, 2=AFTAPE?)
c?  35  ! Playback program version
c?  36  ! Playback program 'sub-version'
c?  37  ! Recorder type (1=GEOS, 2=DR100, ...)
c?  38  ! Recorder version
c?  39  ! Recorder 'sub-version' (GEOS software number)
c?  40  ! Sensor unit serial number
c   41  ! (*) Vertical orientation (degrees)
c   42  ! (*) Horizontal orientation (  "  ) clockwise from North
c?  43-49  ! Sensor model (7A2)
c   50  ! Location number (GEOS)
c   51  ! Experiment or Tape number (GEOS)
c?  52  ! Trigger algorithm type:
c   53  ! Trigger STA (tenths of seconds) (GEOS)
c   54  ! Trigger LTA (seconds) (GEOS)
c   55  ! Trigger ratio STA/LTA 2** (GEOS)
c   56  ! Trigger component no. (GEOS)
c?  57  ! Pre-event memory size (tenths sec.) (GEOS)
c?  58  ! Post-trigger duration (seconds)
c
c  101  ! (*) Bugger processing history
c
c? 208  ! Directory # (study I.D. #)
c? 209  ! Sub-Directory # (or tape-set #)
c  210-216  ! ASCII filename (7A2)
c? 217-219  ! ASCII study name (3A2)
c
c? 252  ! Clock type (GEOS):
c       !    0=None, 1=WWVB, 2=External(master), 3=Manual, INULL=Unknown
c  253  ! Event type (GEOS):
c       !    0=Continuous, 1=Trigger, 2=Preset, 3=Calibration,
c       !    4=Amplifier calibration, 5=Sensor calibration
c  254  ! Motion type:
c       !    1=Acceleration, 2=Velocity, 3=Displacement, 50=Volumetric strain
c  255  ! Component number (1-3:accl, 4-6:vel, 7-9:disp; 1,4,7:vert)
c  256  ! Number of samples in event (only valid when I031 =< 128)

c GEOS/DR100 Header descriptions                       February 27, 1987

cccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccc
c
c  Real*4 header offset:
c
c    1  ! Number of extra real header records
c    2  ! "Undefined" real value (RNULL)
c
c    5  ! Sample rate (Samples per second)
c    6  ! (*) Component sample lag (seconds)
c
c   39  ! (*) Transducer type (A4)
c   40  ! (*) Latitude (Degrees)
c?  41  ! Local coordinate x (Meters)
c   42  ! (*) Longitude (Degrees)
c?  43  ! Local coordinate y (Meters)
c   44  ! (*) Elevation (Meters)
c?  45  ! Local coordinate z: Depth below surface (Meters)
c   46  ! (*) Digitizing constant (Counts/volt)
c   47  ! (*) Anti-alias filter corner frequency
c   48  ! (*) Poles of AAF; roll-off=6dB/pole
c   49  ! (*) Transducer natural frequency
c   50  ! (*) Transducer damping coefficient
c   51  ! (*) Coil constant (Volts/motion-unit)
c   52  ! (*) Amplifier gain (db when I005 = 1)
c
c   60  ! (*) Clock correction (Subtract to get true)
c?  61  ! Seconds since last clock correction
c?  62  ! Voltage
c?  63  ! Desired trigger ratio STA/LTA (real value=2**IBLK(55))
c?  64  ! Actual value of STA at trigger
c?  65  ! Actual value of LTA at trigger
c?  66  ! Maximum value of STA/LTA during event
c
cccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccc

c    ?	! Changes as of August 22, 1986
c    !	! Changes as of February 27, 1987